WKR Task Configuration during GCPEx (Winter 2012) – Last modified: October 16, 2012

|  | CONVOL | DOPVOL1_A | DOPVOL1_B | DOPVOL1_C | POLPPI | DOPVOL2 | CARE RHI | SAT. SITE RHI | SECTOR SCAN |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ANTENNA / RADAR CONTROL |
| Scan Mode | PPI Full | PPI Full | PPI Full | PPI Full | PPI Full | PPI Full | RHI | RHI | PPI Sector |
| Azimuth Resolution (º) | 1 | 0.5 | 0.5 | 0.5 | 0.5 | 1 | 0.2 | 0.2 | 0.5 |
| Elevation | 24 angles | 1 angle @ 0.0 | 1 angle @ 1.5 | 1 angle@ 3.5 | 1 angle @ 0.3 | 1 angle @ 0.0 | 1 angle @ 331 | 4 angles | 12 Angles |
| Scan Speed [deg/sec] | 36 | 5.6 | 5.6 | 5.6 | 6 | 15 | Auto | Auto | 18 |
| Pulse Width [us] | 1.64 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 |
| Polarization | H+V | H+V | H+V | H+V | H+V | H+V | H+V | H+V | H+V |
| PROCESSOR CONFIGURATION |
| Velocity Unfolding | None | 4:3 | 4:3 | 4:3 | 4:3 | None | None | None | None |
| PRF [Hz] (Max/Min) | 400/400 | 1190/892 | 1190/892 | 1190/892 | 1000/750 | 1190/1190 | 1190/1190 | 1190/1190 | 1190/1190 |
| Unamb. Vel [m/s] | 5.3 | 47.6 | 47.6 | 47.6 | 40 | 15.9 | 15.9 | 15.9 | 15.9 |
| Proc. Mode | PPP | RPHASE | RPHASE | RPHASE | PPP | RPHASE | PPP | PPP | PPP |
| Start Range [km] | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Bin Spacing [m] | 250 | 125 | 125 | 125 | 125 | 500 | 125 | 125 | 125 |
| Range Avg/Smth | 4 | 4 | 4 | 4 | 2 | 2 | None | None | 2 |
| Max. Range [km] | 249.83 | 112.4 | 112.4 | 112.4 | 149.9 | 225.5 | 125.96 | 125.96 | 125 |
| Unamb. Range [km] | 374.74 | 125.96 | 125.96 | 125.96 | 149.88 | 126 | 125.96 | 125.96 | 125.96 |
| Samples | 16 | 64 | 64 | 64 | 64 | 80 | 64 | 64 | 64 |
| Filter Dop | None | 3 | 3 | 3 | 3 | 4 | 2 | 2 | 3 |
| Input Bins | 1000 | 900 | 900 | 900 | 1200 | 452 | 1008 | 1008 | 1000 |
| Output Bins | 250 | 225 | 225 | 225 | 600 | 226 | 1008 | 1008 | 500 |
| Data | 2Z, T, V, W, SQI ZDR, Kdp , Phidp, RhoHv | Z, T, V, W | Z, T, V, W | Z, T, V, W | 2Z, T, V, W, SQI ZDR, Kdp , Phidp, RhoHv | Z, T, V, W | 2Z, T, V, W, SQI ZDR, Kdp , Phidp, RhoHv | 2Z, T, V, W, SQI ZDR, Kdp , Phidp, RhoHv | 2Z, T, V, W, SQI ZDR, Kdp , Phidp, RhoHv |
| DATA QUALITY THRESHOLDING |
| T | LOG | LOG | LOG | LOG | LOG | LOG | LOG | LOG | LOG |
| Z | SQI & LOG & CSR | LOG & CSR | LOG & CSR | LOG & CSR | SQI & LOG & CSR | LOG & CSR | LOG &CSR &SQI | LOG &CSR &SQI | LOG &CSR &SQI |
| V | SQI & LOG & CSR | SQI & CSR | SQI & CSR | SQI & CSR | SQI & CSR | SQI & CSR | LOG &CSR &SQI | LOG &CSR &SQI | CSR & SQI |
| W | SQI & LOG & CSR | SIG & SQI & LOG | SIG & SQI & LOG | SIG & SQI & LOG | SQI & CSR | SIG & SQI & LOG | LOG &CSR &SQI | LOG &CSR &SQI | CSR & SQI |
| ZDR | SQI & LOG & CSR | LOG | LOG | LOG | SQI & LOG & CSR | LOG | CSR &SQI | CSR &SQI | LOG & CSR & SQI |
| LOG [dB] | 2.5 | 3 | 3 | 3 | 2 | 1.5 | 2.5 | 2.5 | 2 |
| SIG [dB] | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 |
| CSR [dB] | 25 | 25 | 25 | 25 | 25 | 40 | 40 | 40 | 25 |
| SQI [dB] | 0.05 | 0.4 | 0.4 | 0.4 | 0.05 | 0.4 | 0.05 | 0.05 | 0.05 |
| Speckle | Z, V | Z, V | Z, V | Z, V | Z, V | Z, V | Z, V | Z, V | Z, V |