## Slide 1: GLM Proxy Data Generation: Methods for Stroke/Pulse Level Inter-comparison of Ground-based Lightning Reference Networks
Prepared by
Ken Cummins
Huntsville, AL Sept. 2011

## Slide 2: Context
Requirement
  Ground-base lightning observations are needed to help create GLM proxy datasets over large continental and oceanic regions
  Observations will be provided by a variety of existing and emerging VLF/LF “LLS” datasets
Approaches
  “bulk statistical analysis of datasets at the cell flash-rate level
  Detailed stroke/pulse inter-comparisons to understand what is seen uniquely and in-common by various data sources
Issue
  LLS performance for CG strokes and cloud pulses must be characterized before it can be intelligently applied in quantitative proxy datasets
    Location accuracy
    Detection efficiency
    Type classification (CLD/CG)
  Sub-context: CHUVA LLS inter-comparisons
  Note: Need help from modeling and independent validation where there are no comparison datasets

## Slide 3: Presentation Scope
Description of the inter-comparison tool
Case Study – Japan
Case Study – GLD360
GLD “show and tell”
Next Steps

## Slide 4: What can you detect?
VHF vs. VLF/LF Cloud Flash Detection
The pulses detected by a moderate baseline (~200-300 km) LF/VLF cloud detection system (red dots) generally cluster near the initial breakdown region shown in the 2-D flash depiction using a VHF mapping system (blue dots).
“Reasons” (2/3 - truths)
  VHF emitted during breakdown (spark) and leader processes
  Lower frequencies easily generated by “longer” (time duration and/or channel-length) processes
  Channels must be “substantially vertical” for large EM fields to propagate 100’s of km => significant vertical orientation and depth of charge structure

## Slide 5: What can you detect?
VHF vs. VLF/LF Cloud Flash Detection
Disadvantage of LF/VLF:
  Limited description of the spatial extent of a cloud flash (or the charged regions of a mature thunderstorm)
Benefits:
  Ability to provide reasonable storm onset information
  Quantifiable flash-rate information
  EM signals propagate well through mountainous terrain (no line-of-sight constraint).
  EM signals will be better-correlated with optical emissions observed from space.

## Slide 6: Inter- comparison Tool
Coded in Matlab
Stand-alone executables can run on Unix, Linux, and Windows
Can specify datasets and related parameters in a “cfg” file using a text editor…

## Slide 7: Tool “Outputs”
Analysis “Sheets”
  Sheet 1:
    Requires date, time, lat, lon, and (optionally) type (CG/CLD pulse)
  Sheet 2:
    Requires peak current estimates
  Sheet 3:
    Requires quality-related parameters
      location error estimate
      # sensors reporting the stroke/pulse

## Slide 8: Sheet 1 – Japan Case

## Slide 9: Sheet 2 – Japan Case

## Slide 10: Sheet 3 – Japan Case

## Slide 11: Sheet 1 – GLD360 vs. NLDN (real-time operation)

## Slide 12: Sheet 1 – GLD360 vs. NLDN (Vaisala’s upcoming algorithm release)

## Slide 13: Sheet 2 – GLD360 vs. NLDN (Vaisala’s upcoming algorithm release)

## Slide 14: Sheet 1 – GLD360 vs. NLDN (“bad day” operation – 2 local sensors down)

## Slide 15: Closing Comments/movies
GLD Interpretation
  Real-time data have
    large location errors/scatter
    Many duplicate solutions for the same events
    Poor Ip estimates (not shown)
  Future product generator has
    3-5 km median LA
    ~50%/30% stroke DE over U.S. (good/bad days) => ~80%/60% flash DE)
    Sees many events not reported by the NLDN (low-current strokes and cloud pulses?)
    Good Ip estimates (>90% correct polarity

## Slide 16: Future Directions
Tool
  Spatial map of correlated and uncorrelated datasets
  Spatial DE map accumulated over many days
  Temporal DE curve
  Detailed flash analysis
    Flash DE
    Relative counts of flashes:
      CLD, CG, and CG w/ CLD
Analysis
  Extensive GLD/NLDN comparisons
    Land-only
    Land-to-sea
  Other network inter-comparisons (directed or carried out by NASA/UAH)
  Employ performance values in proxy generator/products
    “up-scale” LLS-based data
    Help understand cell-based datasets and results

## Slide 17: Hurricane Irene August 25-29, 2011
NLDN + IR
GLD360 + IR

## Slide 18: Recent Data (U-of-AZ display)
Western Hemisphere
(Hurricane Katia)
Eastern Hemisphere