TO:  Airborne Science Program            FAX: (202) 358-2770

NASA Headquarters                        Voice: (202) 358-2890

Mail Suite 3F71

Attn: Bruce Tagg

bruce.a.tagg@nasa.gov

Flight Report

| Aircraft : | DC-8 N817NA |
| --- | --- |
| Operating Site(s) From / To : | TISX to KFLL |
| Flight Date : | 8/29/10 |
| Flight Number : | 100609 |
| Take Off Time : | 241:16:30:08 UTC |
| Landing Time : | 242:00:53:44 UTC |
| Flight Time : | 8.5 Hr. |
| Flt Request # / PI: | 108201 / Vasquez |
| Purpose of Flight : | Data [ X ] Ferry [ ] Functional Check [ ] Other [ ] |
| Aircraft Status: | Up [ X ] Down [ ] |
| Sensor Payload : | CAPS, PIP, DAWN, LARGE, LASE, MMS, APR-2, Dropsonde operated. PIP probe had a laser failure early in the mission. 3 dropsondes reported no data after release; 3 dropsondes reported premature loss of data signal after release. |
| Comments : | Dropped 28 sondes. Flight consisted of pattern flown over/through hurricane Earl west of St. Croix at altitudes of 33,000 ft and 37,000 ft. Center of storm was located at approximately 17 20N/59 28W. Descent to 7,000 ft was accomplished northwest of storm area to support atmospheric aerosol measurements. Planned takeoff time was delayed by 2.5 hours due to ingestion of bird into engine #4 during taxi. Engine was inspected for damage, bird debris removed, and cleared for flight in coordinated effort with Dryden Code O management and maintenance personnel. Flight diverted to Ft Lauderdale due to degrading weather forecast for St. Croix. associated with approach of hurricane Earl. |