TO:  Airborne Science Program            FAX: (202) 358-2770

NASA Headquarters                        Voice: (202) 358-2890

Mail Suite 3F71

Attn: Bruce Tagg

bruce.a.tagg@nasa.gov

Flight Report

| Aircraft : | DC-8 N817 NA |
| --- | --- |
| Operating Site(s) From / To : | KFLL to KFLL |
| Flight Date : | 9/13/10 |
| Flight Number : | 100618 |
| Take Off Time : | 18.36.35 UTC |
| Landing Time : | 02.57.17 UTC |
| Flight Time : | 8.5 Hr. |
| Flt Request # / PI: | 108201 / Vasquez |
| Purpose of Flight : | Data [ X ] Ferry [ ] Functional Check [ ] Other [ ] |
| Aircraft Status: | Up [ X ] Down [ ] |
| Sensor Payload : | CAPS, PIP, DAWN, LARGE, LASE, MMS, APR-2, DAWN, and Drop-sondes operated. |
| Comments : | Conducted a survey of system PGI44. All instruments operated successfully. Completed four transects of the center, dropped 21 sondes, all successful. Conducted MMS maneuvers at Mach 0.7 and 32,000 ft. |