## Slide 1: GOES-R GLM Calibration
Bob Iacovazzi Jr.
September 20, 2011
GLM Science Meeting 2011

## Slide 2: GOES-R Calibration Definition
Calibration:
The process to determine factors for converting and correcting raw detector measurements into science data units (e.g., radiance) with the specified level of accuracy. [Calibration requirements are found in MRD Sections 3.4.2.1-7]
GOES-R Program Acronym and Glossary

## Slide 3
GOES-R Program Cal/Val Documents
Roles and
Responsibilities
Technical Details
Notes: Cal/Val Plan & Strategy overarch all of the calibration phases.

## Slide 4: Calibration Support for GLM
  Instrument, Spacecraft and Ground Segments Vendors
  GOES-R Cal/Val Working (CWG) Group Members and Partners
    Flight Project
    Ground Segment Project
    NOAA/NESDIS/STAR
    MIT Lincoln Laboratory
    Field Campaign Support (NASA, NOAA, JPL, etc.)
    Marshall Space Flight Center/UAH

## Slide 5
Calibration Coordination Team (CCT) Formed Under New PSE Leadership
AWG
PSE & Program Science
Flight
GSP
Instr./SC Vendor
GS Vendor
MOST
DOST
GOES-R Calibration Coordination Team
Scope – A coordinating body to ensure efficient implementation of calibration activities throughout the GOES-R Program during all mission phases.
GOES-R Calibration Coordination Team membership diagram
CCT members - Representatives of any group with responsibility to ensure L1b Product integrity, e.g.,
PSE & Program Science
Flight (Deputy Project Manager, Instrument Managers)
Ground (Deputy Project Manager)
Other CWG reps
Vendors (Instrument, Spacecraft and Ground)
MOST (MOM)
DOST (DOM)
AWG
CCT provides a forum to clarify GOES-R cal/val activities and associated member roles and responsibilities
PSE lead has the final authority on cal/val topics

## Slide 6: Major GLM Cal-related Activities in Each Mission Phase
  Pre-Launch
    Schedule determined by Flight and Vendors
      Instrument and Test Design and Review
      Instrument Testing and Test Verification
      L1b Algorithm Development, Implementation and Review
  Post-Launch Testing (PLT)
    Schedule determined by MOST and DOST
      Science Test Design and Review
      Science Tests Analysis and Verification
      Cal Parameter Verification
      Long-Term Monitoring Initialization
      Performance Analysis/Anomaly Resolution
  Mission Operational Lifetime
    Schedule determined by Ops
      Long-Term Instrument and L1b Product Monitoring
      Cal Parameter Updates
      Anomaly Resolution

## Slide 7: Major GLM Cal-related Activities in Each Mission Phase
  Pre-Launch
    Schedule determined by Flight and Vendors
      Instrument and Test Design and Review
      Instrument Testing and Test Verification
      L1b Algorithm Development, Implementation and Review
  Post-Launch Testing (PLT)
    Schedule determined by MOST and DOST
      Science Test Design and Review
      Science Tests Analysis and Verification
      Cal Parameter Verification
      Long-Term Monitoring Initialization
      Performance Analysis/Anomaly Resolution
  Mission Operational Lifetime
    Schedule determined by Ops
      Long-Term Instrument and L1b Product Monitoring
      Cal Parameter Updates
      Anomaly Resolution

## Slide 8: Lockheed-Martin Pre-launch Calibration Overview
GLM is an imager and an event detector and must be radiometrically calibrated for background scenes (images) and for lightning events (optical pulses)
Calibration activities consist of six procedures:
  Static radiometric response (Linearity and uniformity)
  Transient radiometric response (instrument calibration)
  Performance test (detection efficiency, false event rate, etc.)
  Field of view
  Spectral response
  Spacecraft motion and jitter simulation

## Slide 9
Calibration is performed in a class 10K clean room at LMATC
Principal equipment includes
  Large integrating sphere (NIST Certified)
  Integrating sphere with co-aligned optical pulse emitter
  Two precision rotary stages
  Collimator
  Tunable laser
  GLM GSD including a dedicated lightning calibration computer system
Lockheed-Martin Pre-launch Calibration Overview

## Slide 10: Pre-Launch Design & Development Review
Lockheed-Martin
GLM Instrument Manager
GOES-R Portal
Flight / Instrument Vendor Interface
Flight/CWG
Review
Development Plans, Procedures, Reports, Draft CDRLs, RFA Responses, Requested Items
CDRLs, Reports
Reviews, TIMs, and TRRs
Reports, Presentations
Feedback, Comments, Requests, RFAs
CDRLs, Reports
RFA Responses, Requested Items
RFAs
Feedback, Comments,
Requests, Direction, RFAs
Feedback, Comments, RFAs

## Slide 11: Pre-Launch Calibration Data Management
Lockheed-Martin
Cal Testing
Cal Analysis
GLM Instrument Manager
GOES-R Portal
Flight / Instrument Vendor Interface
Flight/CWG
Verification
Selected Cal Reports & Data for CDRLs
Cal Test Data, Results & Reports
Vendor Archive
2030 expiration
All Instrument Test Data
Cal Test Data Requests,
Discrepancy Notification
Cal Test Data Requests,
Discrepancy Notification
Cal Test Data,
Discrepancy Resolution
Cal Test Data, Documentation, Results
Cal Test Validation Reports
Cal/Val Long-term Stewardship

## Slide 12
Lockheed-Martin L1b GPA Development
GOES-R Portal
CLASS
Ground / Ground Segment Vendor Interface
Import: L1b GPA, Test Case IO
Export: L1b GPA Implementation Results
Import: GPA, Test IO, Cal Database, etc.
Export: L1b GPA Review
Harris L1b GPA Implementation
Flight / Instrument Vendor Interface
L1b Ground Processing Algorithm (GPA) Development and Implementation
Export: L1b GPA (CDRLs), Test IO , Description, and Implementation Certification Import: L1b GPA GS Vendor Implementation Results
CWG
TIMs (GSP L1b IPT Chair facilitating)
TIMs (GLM
Instrument Manager Facilitating)

## Slide 13: Major GLM Cal-related Activities in Each Mission Phase
  Pre-Launch
    Schedule determined by Flight and Vendors
      Instrument and Test Design and Review
      Instrument Testing and Test Verification
      L1b Algorithm Development, Implementation and Review
  Post-Launch Testing (PLT)
    Schedule determined by MOST and DOST
      Science Test Design and Review
      Science Tests Analysis and Verification
      Cal Parameter Verification
      Long-Term Monitoring Initialization
      Performance Analysis/Anomaly Resolution
  Mission Operational Lifetime
    Schedule determined by Ops
      Long-Term Instrument and L1b Product Monitoring
      Cal Parameter Updates
      Anomaly Resolution

## Slide 14
Postlaunch Instrument Calibration Data Flow
2-Day Store
Cal Parameter Tables and Algorithms (Wallops only)
NOAA Satellite Operations Facility (NSOF)
L1b Data, GLM L2+ GRB
CLASS
GAS
MM, PG, PD and DE
CWG
Instrument Radiometric, Spectral. Spatial Calibration Data Quality Assurance for GOES Series-R
  Post Launch Verification
  Long-term Instr. Monitoring
  Deep-Dive Calibration Analysis and L1b Product Anomaly Resolution
  Calibration Parameter Updates
Wallops Command and Data Acquisition System (WCDAS)
Fairmount, WV (RBU)
Instrument Calibration Data
GLM Background Images
Calibration-relevant instrument housekeeping & engineering data
L0
Data
L1Data, GLM L2+ GRB
Product Generation Operational Environment
L0 & Input Data
Ground Processing Algorithm
L1b Calibrated
Data
Product Generation Development Environment
L0 & Input Data
Experimental Ground Processing Algorithm
ExperimentalL1b Calibrated
Data
CLASS
Updated Calibration Parameter Tables
Cal L0 and Processing Data
L1b, L2+ Products,
Instr. Cal Data
L0 Data
Instrument Calibration Data
Via
Terrestrial Data Link
MLS

## Slide 15: L1b Product Performance Monitoring and Anomaly Resolution
Anomaly Resolution
Anomaly Resolution
Instr. Telemetry
5-Day RDR
CLASS
WCDAS/RBU-SOZ
NSOF-SOZ
DE in WCDAS SOZ
SOZ-wide Access to Cal Terminals
CALVAL Workstation
Gov’t Tools
MLS
MLS
2-day
GAS
SOZ-wide Access to Cal Terminals
CLASS
External Org
Anomaly Resolution
Org LS
External Org Workstations
Automated Cal Data Acquisition
GOES-R Integrated Cal/Val
Instrument Performance Web Displays
CALVAL Workstation
Gov’t Tools
Org GOES-R Terminals
Org Firewall
L1b, CAL
Product Generation: Product Performance Monitor
Mission Mgmt: GRB Downlink & Monitor
L0
L1b (GRB)
Mission Mgmt: GRB Uplink
Mission Mgmt:
Instr. Temps, etc. H & S Monitor
CAL (RDL)
L1b (GRB)
2-day
L0
Product Generation/ Distribution: Create L0, L0 to L1b processing and GRB generation.

## Slide 16: Post-Launch Calibration Evaluation
Long-term Radiometric Trending
Comparison of GOES-E/W GLM background images
Ratio of GLM background image radiances with ABI and other instruments
GEO-LEO
GEO-GEO
Instrument Performance Monitoring
Tracking of thermal stability of GLM components
Quick views of GLM background images, output every 2.5 minutes

## Slide 17
Long-term Radiometric Trending
Sonoran Desert and White Sands Site Characterization
  Sonoran Desert has been used for GOES Imager long-term radiometric trending
  White Sands is a possible new site for GOES-R
  Characterization of BRDF to remove seasonal signal variation for vicarious calibration.
ER-2 AVIRIS/MASTER Flight Acquisitions Completed: WSMR (May 23, 2011), Sonoran Desert (June 10, 2011)
  Several methods have applicability to determining lifetime GLM radiometric calibration drift:
    Vicarious calibration using deep convective clouds (DCC), sun glint, and deserts
    Radiance bias estimate using NWP and radiative transfer models
Post-Launch Calibration Evaluation

## Slide 18: Summary
GLM calibration leveraging diverse complementary technical capabilities
Comprehensive GOES-R GLM Cal/Val Strategy and Plan developed to ensure product quality
  Pre-launch Vendor implementation and Government review processes for GLM calibration testing and data, and ground processing algorithm
  Post-launch
    GLM calibration-relevant data capture and monitoring to support anomaly resolution
    Long-term calibration trending