## Slide 1
University of Illinois Mobile Rawinsonde Launches during the 2022 IMPACTS Field Campaign Deployment
Andrew Janiszeski1, Troy J. Zaremba1, and Robert M. Rauber1
1University of Illinois Urbana-Champaign
IMPACTS Science Team Meeting | Summer 2022

## Slide 2: Location of Launches
IMPACTS Science Team Meeting | Summer 2022
Site | Latitude | Longitude | Sondes Launched
Geneseo, NY | 42.800 | -77.812 | 4
Plymouth, MA | 41.959 | -70.671 | 5
Albany, NY | 42.687 | -73.853 | 6
Vernon, CT | 41.824 | -72.502 | 4
Plattsburgh, NY | 44.695 | -73.500 | 3
Urbana, IL | 40.116 | -88.253 | 2
Table 1: Launch Site locations IMPACTS 2022
Binghamton
Rawinsonde Launch Locations

## Slide 3: Quality Assessment
IMPACTS Science Team Meeting | Summer 2022
Sondes were checked prior to launch to verify that temperature, relative humidity, and pressure for the sonde were properly referencing surface conditions
  Found one broken sonde and one sonde that was not recording relative humidity
Rawinsondes were iMet-4 Radiosondes that had an accuracy of ±0.2℃ for temperature, ±5% for relative humidity and ±0.2 m s-1

## Slide 4: Data Format
IMPACTS Science Team Meeting | Summer 2022
Field Name | Description | Data Type | Unit
TC | Temperature | float64 | ℃
RH | Relative Humidity | float64 | %
Time | Time in seconds past launch | timedelta64[ns] | ns
HAGL | Height above ground level | float64 | m
PRESS | Pressure | float64 | m s-1
WINDSPD | Wind speed | float64 | mb
WINDDRN | Wind direction | float64 | °
LAT | Latitude | float64 | °
LON | Longitude | float64 | °
Soundings are available to download at: https://search.earthdata.nasa.gov/search?q=uiucsndimpacts/&ghrccloud/data/
Data is in netCDF4 format
  Naming convention: IMPACTS_UIUC_Mobile_research_sounding_YYYYMMDD_hhmm.nc
Attribute information contained in each file includes latitude, longitude, start time, and starting altitude

## Slide 5: How to View Soundings
IMPACTS Science Team Meeting | Summer 2022
Soundings are netCDF4 and do not require any specific software to read in
  Can be easily read into and plotted using Python or Matlab
  Also can be viewed using Panoply
Quick looks are available on the IMPACTS field catalog: http://catalog.eol.ucar.edu/impacts_2022 under Upper Air and then UIUC

## Slide 6: Issues
IMPACTS Science Team Meeting | Summer 2022
There are no known issues or gaps in the data. The only issues we noticed occurred on January 29th
Jan 29th:
18z launch below ~ 800 mb T/Td is likely inaccurate (bad communication)
20z launch has no lat/lon data

## Slide 7: Geneseo, New York - January 17th
IMPACTS Science Team Meeting | Summer 2022
UIUC

## Slide 8: Geneseo, New York - January 17th
IMPACTS Science Team Meeting | Summer 2022

## Slide 9: Albany, New York - February 4th
IMPACTS Science Team Meeting | Summer 2022
UIUC

## Slide 10: Albany, New York - February 4th
IMPACTS Science Team Meeting | Summer 2022

## Slide 11: Hartford, Connecticut - February 13th
IMPACTS Science Team Meeting | Summer 2022
UIUC

## Slide 12: Hartford, Connecticut - February 13th
IMPACTS Science Team Meeting | Summer 2022

## Slide 13: Summary
IMPACTS Science Team Meeting | Summer 2022
The UIUC rawinsonde crew had a successful deployment during the 2022 season
Sampled 7 storms, launching 25 weather balloons
Data is available in the IMPACTS field catalog and we hope people use it in their modeling and observational analysis.

## Slide 14
This analysis implies that orographic cloud seeding effects
Questions?
Contact: janszsk2@illinois.edu, tzaremb2@illinois.edu, r-rauber@Illinois.edu
IMPACTS Science Team Meeting | Summer 2022