## Slide 1: Stony Brook University IMPACTS Ground Observations
Brian Colle1, Pavlos Kollias1,2, and Mariko Oue1
Division of Atmospheric Sciences, Stony Brook University
Environmental and Climate Sciences Department, Brookhaven National Laboratory

## Slide 2: Stony Brook Ground Observations (2020)

## Slide 3: Ka-band Scanning Polarimetric Radar (KASPR)
Available 2019—2021, transmitter failure 2021 (now back in service)
For KASPR, Level 1 on DAAC, but for cases SBU dealiases DV, bias correction for Zdr, and adding Kdp. KASPR reflectivity is well calibrated, but reflectivity (and Zdr) may include attenuations
** KASPR scan strategy: 1 or 2 PPIs– 2 RHIs –VPT– 3 RHIs, repeated every 7-8 min

## Slide 4: Stony Brook University Truck 2020
SBRO
KASPR 30-km range
Cedar Beach
Backscatter lidar
Parsivel2
Met Station
Graw Soundings
MRRPro:
Micro Rain Radar
SKYLER-1: Dual-pol X-band phased-array radar

## Slide 5
Stony Brook GRAW Sounding System
Technical Data | DFM-09 (2020) | DFM-17 (2022)
Weight | <90 g, ready to start | 63 g, ready to start
Size | 200 x 42 x 60 mm | 90 x 67 x 44 mm
Power supply | Lithium | 2 x Lithium CR123A, replaceable
Runtime integrated battery pack | >140 min | > 240 min
Wind finding | GPS (48 channel) | GNSS (GPS/GLONASS/BEIDOU)
Transmission-rate | One full dataset per second | One full data set per second
Bandwidth | < 10 kHz | < 12 kHz
Frequency range | +/- 3 kHz | 400 - 405.99 MHz
Modulation | FSK | GFSK
Output power telemetry | 100 mW, typical | < 100 mW
Error correction telemetry | Code-spreading, interleaving | Code-spreading, interleaving
Temperature resolution | 0.1°C | 0.01 °C (internal)
Temperature accuracy | < 0.2 °C | < 0.2 °C
Humidity resolution | 0.1 %rH | 0.1 %rH
Humidity uncertainty | < 4 %rH | < 4 %rH
Pressure uncertainty | < 0.3 hPa | Uncertainty > 100hPa< 1 hPa Uncertainty 100 - 10hPa< 0.2 hPa Uncertainty < 10hPa< 0.04 hPa
Geopotential height uncertainty | < 10 m | < 8 m
Wind speed uncertainty | <0.2 m/s | < 0.1 m/s

## Slide 6
 | Jan. 18-19 | Jan. 25 | Feb. 7 | Feb. 13 | Feb. 24-26 | Feb. 27
Location | Cedar Beach 40.965N, -73.030E | SBU 40.897N, -73.127E | SBU | Cedar Beach | SBU | SBU
Launch time (UTC) | Jan. 18 181323 Jan. 18 195323 Jan. 18 214620 Jan. 18 235935 Jan. 19 004158 | Jan. 25 175259 | Feb. 7 140738 Feb. 7 174314 | Feb. 13 021656 Feb. 13 050307 Feb. 13 055828 Feb. 13 081120 | Feb. 24 224844 Feb. 25 014604 Feb. 25 154414 | Feb. 27 050442 Feb. 27 081638
2020 Stony Brook Sounding Team Launches
Data QC’d and uploaded to DAAC.

## Slide 7: ROGER (W-band Profiling Radar)
We plan to upgrade the transceiver of the 94-GHz radar using quadratic phase coding (QPC) for high duty cycle operations (i.e., higher sensitivity without multiple-trip interference).
Use of wide bandwidth transmit waveforms to enable ultra-fine range resolution (~1 m), a 30-fold improvement over current instrument.
In addition, a high-performance digital receiver will be added to the radar system to improve its overall performance.
Upgraded in 2022 – now at BNL

## Slide 8: Data Availability for IMPACTS Cases (2020)
* All uploaded to DAAC: sounding, weather station, Pluvio, ceilometer have been QC’d.
 |  | Jan. 18-19 | Jan. 25 | Feb. 7 | Feb. 13 | Feb. 24-26 | Feb. 27
Radar Truck | Location | Cedar Beach 40.965N, -73.030E | SBU 40.897N, -73.127E | SBU | Cedar Beach | SBU | SBU
 | Sounding, Ceilometer, MRR, Parsivel, SKYLER, Weather Station [Sounding time] | ✓ [18/18z, 18/19z, 18/21z, 18/23z, 19/00] | ✓ [17z] | ✓ [14z 17z] | ✓ [02z, 05z, 06z, 08z] | ✓ [24/22z, 25/01z, 25/15z] | ✓ [05z, 08z]
SBU 40.897N, -73.127E | KASPR | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | ROGER | ✓ | ✓ | ✓ | ✓ | ✓ | 
 | Pluvio | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | Parsivel |  |  | ✓ | ✓ | ✓ | ✓
 | MWR |  |  |  |  |  | 
BNL 40.879N, -72.874E | MRR, Ceilometer, Doppler Lidar | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Manhattan 40.728N, -74.007E. | MRR, Ceilometer, Parsivel, Weather station | ✓ | ✓ | ✓ | ✓ | ✓ | ✓

## Slide 9: SKYLER-I was fixed at SBU for IMPACTS 2022
KASPR
Phased-array radar
** KASPR not operational for IMPACTS 2022

## Slide 10
>= 2022: SKYLER-2 dual-polarization X-band phased array radar
Also on truck:
+Radiosonde
+Parsivel
+Met station
* Some data for 17 Jan 2022 (Elmira, NY case)
* Several technical issues have been resolved
Radar was successfully deployed in
Houston TX for ESCAPE/NSF
Variables observed:
reflectivity,
Doppler velocity,
spectrum width,
differential reflectivity,
differential phase,
copolar correlation coefficient,
signal-to-noise ratio,
specific differential phase

## Slide 11
Skyler 3-D Volume Scans (using 91 PPI scans from 1-30 deg elevation)

## Slide 12
12
Ceilometer
HRL
CFMCW
W-band radar
Microrain Radar
New ground site at Brookhaven National Laboratory
94-GHz, MRR-PRO, Parsivel, Pluvio, Ceilometer and HRL Supported by the BNL Center for Multiscale Applied Sensing.
Current (mid-2022 to present – several obs moved BNL
KASPR and MASC located at Stony Brook
All other sensors at BNL

## Slide 13
 | Jan. 7 | Jan. 17 | Jan. 20 | Jan. 29 |  | Feb. 4 | Feb. 13 | Feb. 25 | 
Location | SBU 40.897N, -73.127E | Elmira 42.1742 N -76.8719 E | SBU | SBU | Smith Point 40.7339 N -72.8615E | SBU | SBU | SBU | Fort Edward 43.246 N -73.559 E
Launch time (UTC) | 094323 131258 151019 | 033750 054634 | 124422 | 071954 090813 133618 152741 191951 212657 | 023055 035625 | 195915 | 144210 | 052500 094459 140436 | 061730 083107 150316
2022 Stony Brook Sounding Team Launches

## Slide 14: Deployments and Operations during IMPACTS 2022
All uploaded to DAAC: sounding data QC’d
 |  | Jan. 7 | Jan. 17 | Jan. 20 | Jan. 29 | Feb. 4 | Feb. 13 | Feb.25
Radar Truck | Location | SBU 40.897N, -73.127E | Elmira 42.1742 N -76.8719 E | SBU | Smith Point 40.7339 N -72.8615E | SBU | SBU | Fort Edward 43.246 N -73.559 E
 | Sounding, | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | Ceilometer | Removed |  |  |  |  |  | 
 | MRRPro | Removed |  |  |  |  |  | 
 | Parsivel | ✓ | ✓ | ✓ |  |  | ✓ | ✓
 | SKYLER2 |  | ✓ | ✓ |  |  | ✓ | ✓
 | Weather Station | ✓ | ✓ | ✓ | ✓ |  | ✓ | ✓
SBU 40.897N, -73.127E | KASPR |  |  |  |  |  |  | 
 | ROGER |  |  |  |  |  |  | 
 | SKYLER1 | ✓ | ✓ | ✓ |  | ✓ | ✓ | ✓
 | MRRPro | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | Ceilometer | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | Pluvio | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | Parsivel | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
 | MWR |  |  |  |  |  |  | 

## Slide 15
Questions?
Contact: brian.colle@stonybrook.edu
SBU Sounding Launch 31 Jan 2021