LEONID ACTIVITIES TIMELINE (Peak on 98-321 @ 19:43 +/- 3 hrs)

All times are GMT

November 12, 1998 (98-316):  	ACS System Tables copied to EEPROM (15 tables)

November 13, 1998 (98-317):	S/C System Tables copied to EEPROM (2 tables)

November 14/15, 1998 (317/318):	Final Console review of contingency procedures

November 16, 1998 (98-320):	Begin Increased trending activity schedule for week.

Final Delta-V orbit adjust maneuver prior to Leonid.

November 17, 1998 (98-321):	13:09:30 - 13:29:30 (TDE/SSA2)

Peak Events				No activities scheduled

14:45 - 15:05 (TDE/SSA1)

No activities scheduled

15:46 - 16:06 (TDW/SSA1)

15:42 - 16:38 Exposed to Leonid

LIS Power OFF Procedure to be performed first

VIRS Earth Shield Close Procedure

VIRS Power OFF Procedure next

TMI Power OFF Procedure last - move to next event 					after PR if time runs short.

17:23 - 17:43 (TDW/SSA1)

17:14 - 18:10 Exposed to Leonid

PR OFF Activities (proff.prc):

PR placed in Health Check;

FCIF and RF PS OFF

IPSM2 A/B K7 and K8 relays opened

18:59 - 19:19 (TDW/SSA2)

18:45 - 19:41 Exposed to Leonid

19:37 - 19:57 (TDE/SSA2)

18:45 - 19:41 Exposed to Leonid

20:30 - 20:50 (171/SSA2)

20:16 - 21:13 Exposed to Leonid

21:25 - 21:45 (TDE/SSA2)

Shielded from Leonid for entire event.

22:30 - 22:50 (171/SSA1)

21:48 - 22:44 Exposed to Leonid

November 18, 1998 (98-322):	23:52 - 00:12 (171/SSA1)

PR Power ON activities begin:

Verify temps, Open SCDP relays then close PSM2A 						K7 relay;

Turn on FCIF A and RF PS A;

Place PR in Standby mode;

Enable PR Command Lock;

00:24 - 01:03 (TDE/SSA2)

PR Power ON activities conclude:

TX & RX Phase Code Loads;

Disable PR Command Lock;

Enable PR Time Fix;

PR in Observation Mode;

PR set to 9DB

01:31 - 01:51 (TDW/SSA2)

VIRS Power On

VIRS Outgassing procedure performed:

Door moved to Outgas position;

Scan Drive turned off; 8.5w heater on;

Inner and Intermediate Stage heaters off;

Outgas telemetry mode enabled;

Primary Mounting ring heater on

LIS Power ON procedure to be performed;

03:04 - 03:24 through end of day

TMI Power ON procedure to be performed;

Remaining VIRS activities:

VIRS Intermediate Stage Heater ON when mounting 						ring temp. > 25¡C

VIRS Inner Stage Heater ON when Intermediate 						stage temp. > 298¡K;

VIRS Inner and Intermediate Stage heaters OFF 						when temperatures stabilize;

Mounting ring heater OFF when Intermediate Stage

temp. <220¡K;

VIRS Outgas Telemetry mode disabled

VIRS 15w heater re-enabled

Note1:  VIRS outgassing activity times are 								dependent on telemetry, and may be 								performed during different events than							those shown.

Note2:  The first 12 minutes of each exposure 							period most critical due to SA feathered 							position.

November 19, 1998 (98-323):  	Continue Extra Trending and telemetry analysis

November 20, 1998 (98-324):  	Continue Extra Trending and telemetry analysis

John,

The following are a list of the times that LIS was powered OFF and ON:

321/15:48:01z	/LAPWROF

322/00:52:16z	/LAPWRON

322/00:53:35z	/LTHADJ (with nominal threshold settings)

322/00:54:27z	/LBKGSNDON BG8KBPS

If you need any other times or any data, just let me know.

Candace

****************************************

Candace MM Shoemaker

TRMM Flight Control Services Group Code 453.1

AlliedSignal Technical Services

Phone: (301) 614-5218 or (301) 286-0198

Fax: (301) 614-5266

****************************************