LPVEx extracted SSMIS Temperature Data Records

The LPVEx SSMIS data is extracted from the FNMOC Temperature Data Records (TDR) obtained from NOAA/CLASS.

The original file header has been stripped from the beginning of the data and only data that falls within the area of interest is included here. The criteria for the selection of the data are if any scan position that falls between 15E and 35E with the centre of scan between 45N and 75N.

The original TDR files pose a problem with the start/end point of the orbits, which occur at about 60N. Consequently, the data has been processed to combine two TDR files, removing the 121 scan-line overlap, and extracting the data either side of 60N for the area of interest.

There has been no change to the original data values, nor to the structure of the scan records.

Each scan provides a record of 9592 bytes that relates to brightness temperatures at all frequencies/channels, together with location (latitude/longitude) of scan positions.

The NOAA/CLASS TDR data structure is outlined here:

http://www.ncdc.noaa.gov/oa/rsad/ssmi/swath/ssmis-tdr.pdf

Ignoring the file header, the scan records are comprised of a scan header, ephemeris record, followed by groups of brightness temperatures and latitude/longitudes, finishing with auxiliary data:

| Scan header | 36 bytes |
| --- | --- |
| Ephemeris data | 3x 20 bytes |
| Imager scene | 180x 24 bytes |
| Environmental Scene | 90x 20 bytes |
| Lower Air Sounding Scene | 60x 24 bytes |
| Upper Air Sounding Scene | 30x 16 bytes |
| Auxiliary data | 1456 bytes |
|  | 9592 bytes |

Scan Header:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Year |
| 5 - 8 | Julian Day | Hour | Minute |
| 9 – 12 | Spare | Scan number |
| 13 -16 | Scan Time |
| 17 - | Spare |
|  | Spare |
|  | Spare |
|  | Spare |
| - 36 | Spare |

Ephemeris Data:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Latitude |
| 5 - 8 | Longitude |
| 9 – 12 | Altitude |
| 13 -16 | Julian Day |
| 17 - 20 | Time |

| 21 - 40 | Repeat of above |
| --- | --- |

| 41 - 60 | Repeat of above |
| --- | --- |

Imager Scene:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Ch 8-11 Latitude | Ch 8-11 Longitude |
| 5 - 8 | Scene number | Surface | Rain flag |
| 9 – 12 | Ch 8 Tb | Ch 9 Tb |
| 13 -16 | Ch 10 Tb | Ch 11 Tb |
| 17 - 20 | Ch 17-18 Latitude | Ch 17-18 Longitude |
| 21 - 24 | Ch 17 Tb | Ch 18 Tb |

x180 for each scan position

Environmental Scene:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Ch 12-14 Latitude | Ch 12-14 Longitude |
| 5 - 8 | Scene count | Surface | Ch 12 Tb |
| 9 – 12 | Ch 13 Tb | Ch 14 Tb |
| 13 – 16 | Ch 15-16 Latitude | Ch 15-16 Longitude |
| 17 - 20 | Ch 15 Tb | Ch 16 Tb |

x90 for each scan position

Lower Air Sounding Scene:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Ch 1-7 & 24 Latitude | Ch 1-7 & 24 Longitude |
| 5 - 8 | Scene number | Surface tag |
| 9 – 12 | Ch 1 Tb | Ch 2 Tb |
| 13 – 16 | Ch 3 Tb | Ch 4 Tb |
| 17 – 20 | Ch 5 Tb | Ch 6 Tb |
| 21 - 24 | Ch 7 Tb | Ch 24 Tb |

x60 for each scan position

Upper Air Sounding Scene:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 - 4 | Ch 19-23 Latitude | Ch 19-23 Longitude |
| 9 – 12 | Scene count | Ch 19 Tb |
| 13 -16 | Ch 20 Tb | Ch 21 Tb |
| 17 – 20 | Ch 22 Tb | Ch 23Tb |

x30 for each scan position

Auxiliary Data:

| Bytes |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1-1456 | See above pdf document |

Chris Kidd, NASA/GSFC

25 October 2011

Channel characteristics of F16 SSMIS sensor (after Poe et al., 2001)

| Channel | Center Freq (GHz) | 3-db Width (MHz) | Freq. Stab. (MHz) | Pol. | NEDT (K) | Sampling Interval (km) | No. Scan Positions |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 50.3 | 380 | 10 | V | 0.24 | 37.5 | 60 |
| 2 | 52.8 | 389 | 10 | V | 0.32 | 37.5 | 60 |
| 3 | 53.596 | 380 | 10 | V | 0.33 | 37.5 | 60 |
| 4 | 54.4 | 383 | 10 | V | 0.33 | 37.5 | 60 |
| 5 | 55.5 | 391 | 10 | V | 0.34 | 37.5 | 60 |
| 6 | 57.29 | 330 | 10 | RCP | 0.41 | 37.5 | 60 |
| 7 | 59.4 | 239 | 10 | RCP | 0.40 | 37.5 | 60 |
| 8 | 150 | 1642 (2) | 200 | H | 0.89 | 12.5 | 180 |
| 9 | 183.31±6.6 | 1526 (2) | 200 | H | 0.97 | 12.5 | 180 |
| 10 | 183.31±3 | 1019 (2) | 200 | H | 0.67 | 12.5 | 180 |
| 11 | 183.31±1 | 513 (2) | 200 | H | 0.81 | 12.5 | 180 |
| 12 | 19.35 | 355 | 75 | H | 0.33 | 25 | 90 |
| 13 | 19.35 | 357 | 75 | V | 0.31 | 25 | 90 |
| 14 | 22.235 | 401 | 75 | V | 0.43 | 25 | 90 |
| 15 | 37 | 1616 | 75 | H | 0.25 | 25 | 90 |
| 16 | 37 | 1545 | 75 | V | 0.20 | 25 | 90 |
| 17 | 91.655 | 1418 (2) | 100 | V | 0.33 | 12.5 | 180 |
| 18 | 91.655 | 1411 (2) | 100 | H | 0.32 | 12.5 | 180 |
| 19 | 62.283248± 0.285271 | 1.35 (2) | 0.08 | RCP | 2.7 | 75 | 30 |
| 20 | 60.792668± 0.357892 | 1.35 (2) | 0.08 | RCP | 2.7 | 75 | 30 |
| 21 | 60.792668± 0.357892±0.002 | 1.3 (4) | 0.08 | RCP | 1.9 | 75 | 30 |
| 22 | 60.792668± 0.357892±0.0055 | 2.6 (4) | 0.12 | RCP | 1.3 | 75 | 30 |
| 23 | 60.792668± 0.357892±0.016 | 7.35 (4) | 0.34 | RCP | 0.8 | 75 | 30 |
| 24 | 60.792668± 0.357892±0.050 | 26.5 (4) | 0.84 | RCP | 0.9 | 37.5 | 60 |
|  | RCP = right-hand circular polarization |

Imager scene

Environmental Scene

Lower Air Sounding Scene

Upper Air Sounding Scene