DAWN in GRIP DATA FILE NAMING CONVENTION

grip_dawn_yyyymmdd_df_type_azw_azp_sa_pa_rg_ov_qc

grip_dawn is imposed by GRIP. DAWN stands for the (pulsed, 2-micron, coherent-detection) Doppler Aerosol WiNd (profiling lidar system).

yyyymmdd is date the DC-8 took off, e.g., 20100921. This field is imposed by GRIP

df is the 24 hr format Zulu time of the Data Folder, e.g., 192329

type is the type of data in the file

BROWSE – plot to browse before using data

FSE – Frequency-domain Signal Energy

HWD – Horizontal Wind Direction

HWS – Horizontal Wind Speed/magnitude

TLL – Time vs. Latitude vs. Longitude

TSE – Time-Domain Signal Energy (future)

azw represents the AZimuth angle pattern used in processing Wind

01 – angles -45 and +45 deg

02 – angles -45, -22.5, 0, +22.5, and +45 (future)

azp represents the AZimuth angle used for the signal Energy

01 – angle 0 deg

sa represents number of laser Shots Averaged

pa represents number of scan Patterns Averaged

01 – no scan pattern averaging

rg represents the sample length of the Range Gates

512 – 512 samples per range gate

ov represents the number of OVerlapped samples by two successive range gates

256 – 256 samples overlapped = 50% in the case of 512 samples

qc represents Quality-Controlled data

00 – no quality control

01 – signal power screened data