CPL OPTICAL PROPERTIES (OP) HDF FILE

Definitions of Global Attributes:

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Date | n/a | string | 1 |  | n/a | n/a | Date for this flight |
| Project | n/a | string | 1 |  | n/a | n/a | Field project name |
| NumRecs | n/a | Long integer | 1 |  | 1 | 36000 | Number of horizontal records (profiles) |
| NumBins | n/a | Long integer | 1 |  | 900 | 900 | Number of vertical lidar bins in the optical profiles |
| Frame_Top | km | Float | 1 |  | 20.0 | 23.0 | Top height of CPL reference frame (first bin) |
| Bin_Width | m | Float | 1 |  | 29.0 | 31.0 | Vertical resolution of the lidar |
| NumWave | n/a | Long integer | 1 |  | 3 | 3 | Number of wavelengths in lidar output -- Wavelength (wl) index: 0=355,1=532,2=1064nm |
| Hori_Res | sec | Long integer | 1 |  | 1 | 5 | Horizontal Resolution of the lidar profiles (typically 1 sec or 200 m) |
| PGR | fraction | Float | 1 |  | 0.0 | 2.0 | Polarization gain ratio - 1064nm parallel/perpendicular detector relative calibration used |
| NumChans | n/a | Short integer | 1 |  | 4 | 10 | Total number of lidar channels, including annulus channels if avail, whereas nchan= 4 always |
| MaxLay | n/a | Long integer | 1 |  | 4 | 10 | Maximum number of layers allowed per profile |
| Start_JDay | utc | Float | 1 |  | 0.0 | 366.0 | Decimal julian day for the start time of the flight |
| End_JDay | utc | Float | 1 |  | 0.0 | 366.0 | Decimal julian day for the end time of the flight |

CPL OPTICAL PROPERTIES (OP) HDF FILE

Definitions of Science Data Sets:

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Dim. 3 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Dec_JDay | utc | Double | NumRecs |  |  | 0.0 | 367.0 | Decimal day of year to 5 decimal places (second) for current profile |
| Latitude | degrees | Float | NumRecs |  |  | -90.0 | 90.0 | Latitude of profile, decimal degrees, S= ‘-‘ |
| Longitude | degrees | Float | NumRecs |  |  | -180. | 180. | Longitude of profile, decimal degrees, W= ‘-‘ |
| Gnd_Hgt | km | Float | NumRecs |  |  | -999. | 20.0 | Height of earth’s surface detected by lidar, missing= -999.0 |
| Bin_Alt | km | Float | NumBins |  |  | -20.0 | 25.0 | Altitude in km for each vertical bin |
| Depol_Ratio | n/a | Float | NumBins | NumRecs |  | 0.0 | 1.0 | Final depolarization ratio profile for 1064nm, valid only inside layers |
| Depol_Ratio_Err | n/a | Float | NumBins | NumRecs |  | 0.0 | 1.0 | 1064 nm Depolarization ratio standard deviation profile |
| NumLayers | n/a | Long integer | NumRecs |  |  | 0 | 10 | Number of layers detected in current profile |
| Layer_Type | n/a | Short integer | 10 | NumRecs |  | 0 | 4 | Layer type: 0=missing, 1=PBL, 2=elevated aerosol, 3=cloud, 4= indeterminant |
| Layer_Top_Alt | km | Float | 10 | NumRecs |  | -999. | 22.0 | Heights of all layer tops above mean sea level in profile |
| Layer_Bot_Alt | km | Float | 10 | NumRecs |  | -999. | 22.0 | Heights of all layer bottoms above mean sea level in profile |
| Layer_OD | n/a | Float | 10 | NumWave | NumRecs | -9.9 | 4.0 | Final layer optical depth estimate per layer per wavelength, -8.8=layer not processed, -9.9=invalid |
| Layer_OD_Err | n/a | Float | 10 | NumWave | NumRecs | -9.9 | 4.0 | Final layer optical depth from error profile per layer per wavelength, -8.8=layer not processed, -9-9=invalid |

CPL OPTICAL PROPERTIES (OP) HDF FILE

Definitions of Science Data Sets (Page 2):

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Dim. 3 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Extinction | 1/km | Float | NumBins | NumWave | NumRecs | -9.9 | 100.0 | Extinction profile per wavelength, 0.0=not processed (no layer), -9.9=invalid |
| Extinction_Err | 1/km | Float | NumBins | NumWave | NumRecs | -9.9 | 100.0 | Extinction profile from error profile per wavelength, 0.0=not processed (no layer), -9.9=invalid |
| Lidar_Ratio | Ster- radians | Float | 10 | NumWave | NumRecs | -9.9 | 130.0. | Extinction-to-backscatter ratio used per layer per wavelength, -8.8=layer not processed, -9.9=invalid |
| Lidar_Ratio_Err | Ster- radians | Float | 10 | NumWave | NumRecs | -9.9. | 130.0 | Lidar ratio from error profile per layer per wavelength, -8.8=layer not processed, -9.9=invalid |
| Direct_OD | n/a | Float | 10 | NumWave | NumRecs | -9.9 | 4.0 | Optical depth estimate from transmission loss only per layer per wavelength, not final od of layer, -8.8=layer not processed, -9.9=invalid |
| Inver_Type | n/a | Short integer | 10 | NumWave | NumRecs | -1 | 1 | Type of lidar inversion used, -1=missing, 0=backward, 1=forward |
| LRatio_Source* | n/a | Short integer | 10 | NumWave | NumRecs | 0 | 9 | Source of lidar ratio calculation per layer per wavelength (see explanation below table)* |
| Plane_Alt | km | Float | NumRecs |  |  | -999. | 20.0 | Height of the aircraft above mean sea level, missing= -999.0 |
| Plane_Pitch | degrees | Float | NumRecs |  |  | -180. | 180. | Aircraft pitch, decimal degrees, down= ‘-‘ |
| Plane_Roll | degrees | Float | NumRecs |  |  | -180. | 180. | Aircraft roll, decimal degrees, left turn= ‘-‘ |
| Mol_Ext_Prof | 1/km | Float | NumBins | NumWave |  | 0 | 10^-3 | Rayleigh extinction profile of first record, currently used for whole flight |

CPL OPTICAL PROPERTIES (OP) HDF FILE

Definitions of Science Data Sets (Page 3):

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Dim. 3 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| T_Loss_Stats | n/a | Short integer | 10 | NumWave | Num Recs | 0 | 7 | Layer transmission loss technique statistics, 0=passed test, 1=no ground return after this final layer, 2=no lower layer or ground return, 3=clear zone below layer too small, 4=clear zone SNR below minimum, 5=transmission^2 of bin below minimum, 6=transmission^2 of layer <= 0.0, 7=1064nm S ratio used 532 optical depth |

*Source of Lidar ratio calculation per layer per wavelength:

Aerosols:

0=pre-defined default wavelength-dependent equations based on general geographic location and rh

1=educated guess based on recent aerosol history at location (PBL)

2=calculated from available column AOD at location and time

3=pre-calculated from AERONET, CPL, etc. for location and time

4=retrieved directly using technique calculating layer transmission loss

5=future use

6=lowered by a maximum of 5.0sr in order to process down to layer bottom (excludes 4)

7&8=future use

9=missing

Clouds:

0=water phase determination based on met temperature profile only, used wavelength dependent equation based on mean layer temperature

1= same as 0 except phase determination based on depolarization ratio and temperature

2=future use

3=1064nm S ratio calculated from 532nm optical depth using transmission loss technique

4=retrieved directly using technique calculating layer transmission loss

5=calculated setting layer bottom transmission to reflect extinguished signal

6=lowered by a maximum of 5.0sr in order to process down to layer bottom (excludes 3,4,5)

7&8=future use

9=missing