# Content of “namma_apr2_yymmdd_hhmmss_41.hdf”

# 1. Data Format (version 4.1)

Note: the yymmdd_hhmmss field in the filename indicates the UTC start time of the data.

| Name | format | size | Notes |
| --- | --- | --- | --- |
| fileheader | int32 | 18 |  |
| scantime | int32 | nscan x nray | Beginning of scan in seconds since 1 January 1970 |
| scantimus | int32 | nscan x nray | Beginning of scan: microseconds past scantime |
| lat | float | nscan x nray | From P-3 navigation files |
| lon | float | nscan x nray | From P-3 navigation files |
| roll | float | nscan x nray | From P-3 navigation files |
| pitch | float | nscan x nray | From P-3 navigation files |
| drift | float | nscan x nray | From P-3 navigation files |
| alt_nav | float | nscan x nray | From P-3 navigation files (meters) |
| alt_radar | float | nscan x nray | From APR-2 surface echo (meters) |
| look_vector | double | nscan x nray x 3 | From P-3 navigation files |
| look_vector_radar* | double | nscan x nray x 3 | From APR-2 surface echo |
| range0 | float | nscan x nray | Distance of the first radar range bin from a/c |
| isurf | int32 | nscan x nray | Index of radar range bin intersecting surface (starting from 0). |
| sequence | int32 | nscan x nray | Ray number within the file |
| v_surfdc8 | float | nscan x nray | Apparent surface Doppler velocity as estimated from P-3 navigation |
| v_surf | float | nscan x nray | APR-2 measured surface Doppler velocity |
| beamnum | float | nscan x nray | Ray number within a scan |
| surface_index | float | nscan x nray | Preliminary surface classification index |
| zhh14 | int16 | nscan x nray x nbin | Radar Reflectivity at Ku band (scaled dBZ) |
| zhh35 | int16 | nscan x nray x nbin | Radar Reflectivity at Ka band (scaled dBZ) |
| ldr14 | int16 | nscan x nray x nbin | Linear Depolarization Ratio (scaled dB) |
| vel14 | int16 | nscan x nray x nbin | Doppler Velocity at Ku band (scaled m/s) |

nscan is the number of scans in a file, nray is the number of rays, or beams, within a scan, and nbin is the number of bins within a ray.  The fileheader is stored as Vdata; the remaining items are Scientific Data Sets (SDSs).  The last 3 items in Table 3 are the APR-2 reflectivity and Doppler data.

Missing data are replaced by –9999.

Altitude and Look Vector (i.e., the 3 components of the antenna relative to a global coordinate system with x being the aircraft ground track and z being vertical) are provided in two estimates: alt_nav and look_vector are calculated relying on the aircraft navigation information, instead alt_radar and look_vector_radar are calculated relying on the observed surface return in APR-2 data.   The latter pair is reliable only when flying over ocean, and in this case it provides a more accurate geolocation than the navigation-based pair.

The predicted and observed surface Doppler velocities are also provided, the latter was corrected for occasional aliasing and, in turn, it was used to correct the Doppler measurements of precipitation for the bias introduced by the aircraft motion.

The surface index is estimated by analyzing APR-2 surface return (roughness, angle dependence of the surface normalized radar cross section, apparent surface inclination and LDR at nadir). It assumes one of 6 values (this classification is preliminary, see next section for known issues):

- 0 = Rough land

- 1 = Ocean (level flight)

- 2 = Ocean (roll maneuver)

- 3 = Flat land (level flight)

- 4 = Flat land (rolling maneuver)

- 5 = Antenna not scanning (unknown surface)

The file header contains information about the APR-2 data.  These are parameters that are constant over the entire file. Table 4 shows the file header.

A sample Matlab routine is available for reading APR-2 HDF data.  FORTRAN or C code can also be constructed using the HDF libraries available from NCSA.

File header

# 2. Known Problems, issues and other notes

This section lists all known problems with the APR-2 namma v4.1 data.

Some of these problems are caused by problems in the raw data, while others are processing problems.

- External calibration was used for all products. Reflectivity measurements should be considered reliable within (1.0 dBZ in this release. Mean normalized surface cross section at 10 degrees and Ku-band incidence is estimated at 6.7dB: this value is about 0.5 dB lower than the generally accepted standard.

- Improved noise subtraction has allowed to lower the Ka-band minimum detectable reflectivity to about -1dBZ at 10 km. The low range of dBZ is visible in the browse images associated with this release as purple. Thresholding was kept just below the noise floor max to maximize use of the Ka-band data: noise contribution is visible in some files.

- IMPORTANT: radar reflectivity factors are as measured – no correction for path attenuation is included in these products.

- The radar altitude and look_vector are occasionally affected by aircraft motion at a sub-scan timescale. This data version was produced using the 1Hz navigation data from DC-8.  MMS 20 Hz data are planned for the next data release.

- No data are available from the 24th ray of each scan (beamnum = 1). This ray was used for noise measurements (no pulse transmitted). The 24th ray was included in this dataset solely for compatibility with APR-2 datasets from previous experiments.

- LDR estimates are included in this release for the Ku-band channel. Users are cautioned in interpreting very low values of LDR (e.g., less than -20 dB) which are characterized by larger overall uncertainty.

- Antenna and range sidelobes show up as artifacts in data in some cases (i.e., thin feature at constant range appearing at large scan angles a few hundred m above the surface).

- Occasionally, high lateral winds caused the Doppler measurements to be aliased. Doppler measurements should be corrected accounting for a maximum unambiguous velocity of (27.5 m/s. Also, correction for aircraft motion is less reliable when the aircraft was maneuvering or was affected by turbulence. Correction for aircraft motion over land is not reliable.

- The surface_index is estimated on a scan-by-scan basis. The most frequent misclassification is ocean being classified as flat land.

- The following data fields are present but are not used in the HDF files: ka_begin, ka_end and vsurf (note: v_surf replaces it). Users should ignore them.

- The isurf index is occasionally misdetected because of extreme attenuation in the rain profile: however these misdetections have been significantly reduced in number with respect to version 4.

- Ka-band TWTA had occasional faults, missing data are replaced by –9999.

- Occasional ‘locks’ in the antenna scanning occurred. They are indicated by the value 5 in surface index product.

- Browse images are vertical slices below the aircraft. Effects of horizontal advection across the vertical plane are sometimes relevant to the interpretation of the images: users are invited to inspect the 3-D data fields for files of interest.

# 3.  Contact Information

This data is intended for research rather than operational use, and users should contact the APR-2 team regarding its use, especially before publication or public presentation.

This is the second release of APR-2 data from NAMMA 2006: these products that are still undergoing validation and quality control. Users are invited to address questions and provide feedback to the contact below.

Contact information:

Simone Tanelli: simone.tanelli@jpl.nasa.gov