HIRAD data are provided for flights over Earl (late 1 - early 2 Sept 2010) and Karl (16 Sept 2010).

V0 data available for this first release contains the brightness temperature (Tb) at 5 GHz.   Rain rate and wind speed were added to this dataset in May 2013.   V1 brightness temperatures were released in December 2015; however, rain rates and wind speed will still need to be retrieved from the V0 data.

See the enclosed Powerpoint file for descriptions of the data and information about flight legs.

V0 data are in Matlab (*.mat) and netcdf (*.nc) formats.

V0 data are organized into directories for each flight, and then by data files and image files. Additionally, there is a directory "filtered" in which is placed images and data after each swath (leg) is treated with a cross-track filter to remove artifacts that are present due to unresolved instrument calibration issues.  The filter is described in the enclosed Matlab script ("read_plot_filterTB_HIRAD.m"), which can be viewed as a simple text file to infer the filtering technique, even if the user does not have Matlab.