CPL ATTENUATED TOTAL BACKSCATTER (ATB) HDF FILE

Definitions of Global Attributes:

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Date | n/a | string | 1 |  | n/a | n/a | Date for this flight |
| Project | n/a | string | 1 |  | n/a | n/a | Field project name |
| NumRecs | n/a | Long integer | 1 |  | 1 | 36000 | Number of horizontal records (profiles) |
| NumBins | n/a | Long integer | 1 |  | 900 | 900 | Number of vertical lidar bins in the optical profiles |
| Frame_Top | km | Float | 1 |  | 20.0 | 23.0 | Top height of CPL reference frame (first bin) |
| Bin_Width | m | Float | 1 |  | 29.0 | 31.0 | Vertical resolution of the lidar |
| NumWave | n/a | Long integer | 1 |  | 3 | 3 | Number of wavelengths in lidar output -- Wavelength (wl) index: 0=355,1=532,2=1064nm |
| Hori_Res | sec | Long integer | 1 |  | 1 | 5 | Horizontal Resolution of the lidar profiles (typically 1 sec or 200 m) |
| NumChans | n/a | Short integer | 1 |  | 4 | 10 | Total number of lidar channels, including annulus channels if avail, whereas nchan= 4 always |
| MaxLay | n/a | Long integer | 1 |  | 4 | 10 | Maximum number of layers allowed per profile |
| Start_JDay | utc | Float | 1 |  | 0.0 | 366.0 | Decimal julian day for the start time of the flight |
| End_JDay | utc | Float | 1 |  | 0.0 | 366.0 | Decimal julian day for the end time of the flight |

CPL ATTENUATED TOTAL BACKSCATTER (ATB) HDF FILE

Definitions of Science Data Sets:

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Dim. 3 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Dec_JDay | utc | Double | NumRecs |  |  | 0.0 | 367.0 | Decimal day of year to 5 decimal places (second) for current profile |
| Latitude | degrees | Float | NumRecs |  |  | -90.0 | 90.0 | Latitude of profile, decimal degrees, S= ‘-‘ |
| Longitude | degrees | Float | NumRecs |  |  | -180. | 180. | Longitude of profile, decimal degrees, W= ‘-‘ |
| Gnd_Hgt | km | Float | NumRecs |  |  | -999. | 20.0 | Height of earth’s surface detected by lidar, missing= -999.0 |
| Bin_Alt | km | Float | NumBins |  |  | -20.0 | 25.0 | Altitude in km for each vertical bin |
| Saturate | km | Float | NumChans | NumRecs |  | -5.0 | 23.0 | Height where detector saturation occurred per channel, no saturation= -5000.0 |
| Depol_Ratio | n/a | Float | NumBins | NumRecs |  | 0.0 | 1.0 | Final depolarization ratio profile for 1064nm, valid only inside layers |
| NumLayers | n/a | Long integer | NumRecs |  |  | 0 | 10 | Number of layers detected in current profile |
| Layer_Type | n/a | Short integer | 10 | NumRecs |  | 0 | 4 | Layer type: 0=missing, 1=PBL, 2=elevated aerosol, 3=cloud, 4= indeterminant |
| Layer_Top_Alt | km | Float | 10 | NumRecs |  | -999. | 22.0 | Heights of all layer tops above mean sea level in profile |
| Layer_Bot_Alt | km | Float | 10 | NumRecs |  | -999. | 22.0 | Heights of all layer bottoms above mean sea level in profile |
| Plane_Pitch | degrees | Float | NumRecs |  |  | -180. | 180. | Aircraft pitch, decimal degrees, down= ‘-‘ |
| Plane_Roll | degrees | Float | NumRecs |  |  | -180. | 180. | Aircraft roll, decimal degrees, left turn= ‘-‘ |

CPL ATTENUATED TOTAL BACKSCATTER (ATB) HDF FILE

Definitions of Science Data Sets (Page 2):

| Parameter Name | Units | Data Type | Dim. 1 | Dim. 2 | Dim. 3 | Min Value | Max Value | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Plane_Alt | km | Float | NumRecs |  |  | -999. | 20.0 | Height of the aircraft above mean sea level, missing= -999.0 |
| ATB_355 | km-1 sr-1 | Double | NumBins | NumRecs |  | 10^3 | 10^5 | Attenuated total backscatter profile for 355 nm for each record |
| Cali_355 | km^3/Js^2 | Double | NumRecs |  |  | -9.9 | 10^6 | Calibration constant at 355 nm for each record |
| ATB_532 | km-1 sr-1 | Double | NumBins | NumRecs |  | -1.0 | 10.0 | Attenuated total backscatter profile for 532 nm for each record |
| Cali_532 | km^3/Js^2 | Double | NumRecs |  |  | 10^4 | 10^6 | Calibration constant at 532 nm for each record |
| ATB_1064 | km-1 sr-1 | Double | NumBins | NumRecs |  | -1.0 | 10.0 | Attenuated total backscatter profile for 1064 nm for each record |
| Cali_1064 | km^3/Js^2 | Double | NumRecs |  |  | 10^3 | 10^5 | Calibration constant at 1064 nm for each record |
| Pressure | hPa | Short integer | NumBins |  |  | 0 | 1100 | Atmospheric pressure profile of first record, currently used for whole flight |
| Temperature | C | Float | NumBins |  |  | -100 | 100. | Atmospheric temperature profile of first record, currently used for whole flight |
| RH | % | Float | NumBins |  |  | 0.0 | 100. | Atmospheric relative humidity profile of first record, currently used for whole flight |
| Mol_Back | km-1 sr-1 | Float | NumBins | NumWave |  | 0 | 10^-2 | Rayleigh backscatter profile of first record, currently used for whole flight for all 3 wavelengths |